## Slide 1: VIRTUAL PROCESS HEATING INPLT Session 8

## Slide 2
Company Name:
Facility Name:
Participant Name(s):

## Slide 3: Process Heating Equipment at the Facility
At our facility we use the following process heating equipment:
Pusher Furnace
Cold Mill Annealing Oven
Melter # 4
Recycle G Furnace
Soaking Pit

## Slide 4: Prescreening Results
Annual Energy Use
Annual Energy Cost

## Slide 5: Pusher Reheat Furnace Energy Assessment
Measured furnace wall temperatures using infrared pyrometer
Measured furnace emissions parameters using Testo 340 analyzer
Used OEM blueprints and technical specifications to get furnace information
Most data taken from active HMI screens and available historical data
What data measured/collected

## Slide 6: Baseline Energy/Heat Balance

## Slide 7: Energy Savings in Process Heating
Areas of Energy Use and Possible Improvements
Heat generation Combustion System
Furnace Walls
Water or air cooling (if any)
Furnace Exhaust and Heat Recovery
4
3
5
Other Energy Losses
10
Openings Furnace Doors etc.
6
Material Handling
2
Load/Charge Material
1
Control System
8
Auxiliary Systems
9
7

## Slide 8: Potential Energy Saving Opportunities Identified
Raise charge material temperature into furnace
  Consider possible options
Raise combustion air temperature
  Return recuperator to OEM specifications
  Increase air heat transfer efficiency through recuperator (updated recuperator)
Heat lost through furnace walls
  Repair existing furnace refractory
  Update furnace refractory material

## Slide 9: Opportunity # 1 - Raise charge material temperature into furnace
Theoretical calculations (Billet inlet average temperature 250 deg. F.)
  Energy Savings 68,183 MMBTU/year
  Energy Cost Savings $272,730 year

## Slide 10: Opportunity # 2 - Raise combustion air temperature
Raise Temp from 661°F Today to 710°F OEM
  Energy Savings 11,470 MMBTU/year
  Energy Cost Savings $45,870 year

## Slide 11: Opportunity # 3 - Reduce heat loss through walls
Reduce average wall temperature from 427°F to 200°F
    Energy Savings 93,930 MMBTU/year
    Energy Cost Savings $375,715 year,

## Slide 12: Summary of Energy Savings Opportunities
Total Savings Summary
Use graphs from the MEASUR tool

## Slide 13: Next Steps or Action Items after the PH VINPLT
What are your next steps to implement opportunities?
What are you planning to do after the PH VINPLT?
Lessons learned?

## Slide 14: Questions and Answers